## Slide 1: Functional Approach in Self-Timed Circuit Design
Plekhanov Leonid, Zakharov Victor, Stepchenkov Yuri
Institute of Informatics Problems, Federal Research Center "Computer Science and Control" of the Russian Academy of Sciences, IPI RAS, Moscow, Russian Federation
IPI RAS EWDTS-2015 1

## Slide 2: Contents
Event-driven analysis of SI-circuits
Functional analysis of SI-circuits:
  Low level analysis
  High level analysis
Synthesis of SI-circuits
Conclusions
IPI RAS EWDTS-2015 2

## Slide 3: Essence of event-driven analysis
IPI RAS EWDTS-2015 3
Analyzed circuit should be presented in a closed feed-back form: only outputs and feed-backs
Analyzed circuit
Feed-back

## Slide 4: Problems of event-driven analysis
IPI RAS EWDTS-2015 4
Analysis is carried out only for one initial state – completeness is far of practical needs
Exponential dependence of the computational complexity on the number of elements and degree of parallelism

## Slide 5: Event-driven analysis: Change Diagrams, part 1
IPI RAS EWDTS-2015 5
Circuit | Micro-pipeline control queue |  | Asynchronous switch | 
CAD Tool | Time, sec | Memory / disk swaping | Time, sec | Memory
TRANAL | 180 | 400 Kbytes /+ | 0.28 | 100 Kbytes
VERDECT | 300 | 22 Mbytes /– | 0.99 | 122 Kbytes
TRASPEC | 1 | 100 Kbytes /– | 0.38 | 100 Kbytes

## Slide 6: Event-driven analysis: Change Diagrams, part 2
IPI RAS EWDTS-2015 6
CAD tools | Paral-lelism | Circuit level | Memory for state, Gbyte | Number of states per hour, 106
TRANAL | 5-6 | cells | 0.64 | 0.3
BTRAN | 12-16 | modules | 2 | 1.0
ASYAN | 18 -24 | blocks | 48 | 200

## Slide 7: Event-driven analysis: software tools from IPI RAS
IPI RAS EWDTS-2015 7
Unit's type – capacity / parallelism | Analysis time, min*) |  | 
 | BTRAN | ASYAN | ASPECT
Binary counter – 4 / 1 | 0.01 | 0.12 | 0.02
Shift register – 4 / 4 | 0.21 | 0.97 | 0.02
Microcore – 4 / 47 | − | 0.53 | 0.02
ALU – 64 / 293 | − | − | 0.14
Divider – 16 / 330 | − | − | 1588
Divider – 64 / 1024 | − | − | 27360
*) for single state of inputs and triggers

## Slide 8: Functional approach
IPI RAS EWDTS-2015 8
Analyzes the equations of circuits
Deals with the open circuits
Takes into account a nature of speed-independent circuits:
  ST-coding of data
  Two-phase operation discipline (work phase and spacer one)
  Signal indication, and so on

## Slide 9: Functional approach: SI circuit definition
IPI RAS EWDTS-2015 9
Absence of races for any finite delay of the elements
Indicativeness of all inputs, outputs and internal signals
An open circuit possessing two features:

## Slide 10: Functional approach: hierarchical analysis
High levels: structural description
IPI RAS EWDTS-2015 10
Lower level: logical function description
…
Top level
Block 1
Block N
Unit 1
Unit 2
Unit M
…

## Slide 11: Low level analysis
IPI RAS EWDTS-2015 11

## Slide 12: Low level analysis: races control
IPI RAS EWDTS-2015 12

## Slide 13: Low level analysis: races control
IPI RAS EWDTS-2015 13

## Slide 14: Low level analysis: races control
IPI RAS EWDTS-2015 14

## Slide 15: Low level analysis: connection control
IPI RAS EWDTS-2015 15

## Slide 16: High level analysis: checking lists & attributes
IPI RAS EWDTS-2015 16
Hierarhical approach on base of verified low level units
Verifying connections
Verifying indicativeness
Verifying absence of races
Preparing descriptions for next analysis level

## Slide 17: Functional analysis via Event-driven analysis
IPI RAS EWDTS-2015 17
Unit's type – capacity / parallelism | Analysis time, min | 
 | ASPECT*) | FAZAN
Microcore – 4 / 47 | 0.02 | 0.01
*) for single state of inputs and triggers

## Slide 18: Synthesis of SI circuits
Based on logical functions that are not self-timed
Balanced by performance and complexity
Minimized indication circuit
Software tools
IPI RAS EWDTS-2015 18

## Slide 19: Synthesis of SI circuits
F1 = A  B, F2 = B  C
V1 = A  B, V2 = B  C,
VB1 = AB  BB, VB2 = BB  CB,
indications
I1 = A  AB, I2 = B  C  BB  CB
IPI RAS EWDTS-2015 19

## Slide 20: Conclusions
The functional approach provides the following advantages:
  Analysis of SI-feature of open circuits
  Hierarchical SI-analysis of VLSI and SoC
  Synthesis of combinational circuits with dual-rail signals by given criterion of performance or complexity
IPI RAS EWDTS-2015 20

## Slide 21: Thanks!
IPI RAS EWDTS-2015 21

## Slide 22: Contacts
  Director: academician Sokolov I.A.
Address: Institute of Informatics Problems of the Federal Research Center "Computer Science and Control" of the Russian Academy of Sciences (IPI RAS), Moscow, Russian Federation, 119333, Vavilova str., 44, b.2
Tel: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: ISokolov@ipiran.ru
Stepchenkov Y.A., tel. +7 (495) 671 15 20, Ystepchenkov@ipiran.ru
IPI RAS EWDTS-2015 22