## Slide 1: Cell Library for Speed-Independent VLSI
Stepchenkov Yuri, Zakharov Victor, Rogdestvenski Yuri, Diachenko Yuri, Morozov Nickolai, Stepchenkov Dmitri
Institute of Informatics Problems, Federal Research Center "Computer Science and Control" of the Russian Academy of Sciences, IPI RAS, Moscow, Russian Federation
IPI RAS EWDTS-2015 1

## Slide 2: Contents
Main features of SI-circuits
Content of the cell library
Interface cells
Cells with forced outputs
Indication cells
Characterization and approbation
Conclusions
IPI RAS EWDTS-2015 2

## Slide 3: Main features of SI-circuits
IPI RAS EWDTS-2015 3
Speed-Independent (SI) circuits excel synchronous ones in:
Robustness to variation of electrophysical parameters or to their degradation
Operation safety and validity of the data processing results
High performance, that is maximum possible at any real environment and data

## Slide 4: Experience in SI-circuits
IPI RAS EWDTS-2015 4
4-Bit Microcontroller core (analog of PIC18)
Complexity is greater by factor of 1.43,
Workability range (S=U*T) is wider by factor of 16,
Performance is higher by factor of 3.25

## Slide 5: Peculiarities of SI-circuits
IPI RAS EWDTS-2015 5
Two-phase discipline: work and spacer (pause)
Indication of each operation phase
Acknowledge-require technique of interaction between SI-units
An arbitrary duration of each phase

## Slide 6: Specific circuit base for SI-units
IPI RAS EWDTS-2015 6
All cells for designing SI-circuits must be single-stage one or have an output indicating all interior signals
Their inputs and outputs take only logical 0 and 1 values

## Slide 7: Library’s content
IPI RAS EWDTS-2015 7
Combinational logic
Triggers
Counters
Multiplexers
Adders
Code converters
Indicators

## Slide 8: Bit of binary counter
IPI RAS EWDTS-2015 8
T, TO – complementing input and output; C, P – preset inputs; I – indicator

## Slide 9: Interface cells: latch
IPI RAS EWDTS-2015 9
D – unary data input; E – write enable input with null spacer; R – asynchronous reset

## Slide 10: Interface cells: flip-flop
IPI RAS EWDTS-2015 10
D – unary data input; E – write enable input with null spacer; R – asynchronous reset

## Slide 11: Interface cells: flip-flop
IPI RAS EWDTS-2015 11
D – unary data input; E – write enable input with unit spacer; R – asynchronous reset

## Slide 12: Cells with forced output: latch
IPI RAS EWDTS-2015 12
R, S – dual-rail data input; C – self-timed reset; Q, QB – bi-phase forced output

## Slide 13: Cells with forced output: flip-flop
IPI RAS EWDTS-2015 13
R, S – dual-rail data input; C – self-timed reset; Q, QB – forced output

## Slide 14: Indication cells: hysteresis triggers
IPI RAS EWDTS-2015 14
I0, I1 – indication signals

## Slide 15: Indication cells: combined logic
IPI RAS EWDTS-2015 15
I0, I1 – indication signals;
B*,B*B – bi-phase data signals

## Slide 16: Library characterization
IPI RAS EWDTS-2015 16
Self-timed feature analysis (ASPECT)
Automatic calculation of the electrical and timing parameters (STERH)
Model files in LIBERTY and Verilog formats (STERH)
Integration with modern industrial CADs

## Slide 17: Cell library approbation
IPI RAS EWDTS-2015 17
Various CMOS standard processes:
  1.5 μm for semicustom circuits (Microcore, 14 000 transistors),
  0.18 μm for semicustom circuits (Microcore, 17 000 transistors),
  0.18 μm for custom VLSI (Square-Root & Divider, 77 000 transistors),
  65 nm for custom VLSI (Square-Root & Divider, 77 000 transistors; Fused Multiply-Add Unit, 315 000 transistors)

## Slide 18: Cell library approbation
IPI RAS EWDTS-2015 16
Functional description (VHDL, Verilog)
SI-VLSI CADs
Kovcheg
ASPECT
ASYAN
FAZAN
TASKAN
SYNTABIB
САМАН
25 registered programs
SI-cell Libraries
20 RF patents
2 USA patents
Special-purpose and Test SI-VLSI
Microcontroller Core (CMOS GA 5503)
Coder-Decoder (CMOS GA
5507/5521)
Increase of steady operation range (10-15 times); decrease of energy consumption (30-50%); rise of performance (100-250%); detection of constant malfunctions (up to 100%)
ST-circuitry: methodology, libraries, CAD tools, implementation
Divider & Square-Rooter (180-nm, 65-nm CMOS)
Fused Multiply-Add (180-nm, 65-nm CMOS)
GA 5507
GA 5503
GA 5529
GA 5521
180 nm
65 nm

## Slide 19: Conclusions
Suggested library:
  Corresponds to the criteria of building SI-circuits,
  Contains more than 200 library cells expanding standard cell libraries,
  Provides really SI solutions for interfacing with synchronous environment and for driving large loads
IPI RAS EWDTS-2015 19

## Slide 20: Thanks!
IPI RAS EWDTS-2015 20

## Slide 21: Contacts
IPI RAS EWDTS-2015 21
  Director: academician Sokolov I.A.
Address: Institute of Informatics Problems of the Federal Research Center "Computer Science and Control" of the Russian Academy of Sciences (IPI RAS), Moscow, Russian Federation, 119333, Vavilova str., 44, b.2
Tel: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: ISokolov@ipiran.ru
Stepchenkov Y.A., tel. +7 (495) 671 15 20, Ystepchenkov@ipiran.ru