## Slide 1
DSP filter kernels preliminary benchmarking for recurrent data-flow architecture
Institute of Informatics Problems, Federal Research Center
"Computer Science and Control" of Russian Academy of Sciences
Yu. Stepchenkov, D. Khilko, Yu. Shikunov, G. Orlov
The study was done by a grant from the Russian Science Foundation (Project №. 19-11-00334)

## Slide 2: Why is benchmarking needed?
The prototype has been synthesized
It has been tested on Isolated Word Recognition task
Further and more precise tests are required
Notes: Hybrid architecture with primitive control unit and main DSP processor.

## Slide 3: BDTI Kernel Benchmarks
Function | Function Description | Example Applications
Real Block FIR | Finite impulse response filter that operates on a block of real (not complex) data. | Speech processing (e.g., G.728 speech coding).
Complex Block FIR | FIR filter that operates on a block of complex data. | Modem channel equalization.
Real Single-Sample FIR | FIR filter that operates on a single sample of real data. | Speech processing, general filtering.
LMS Adaptive FIR | Least-mean-square adaptive filter; operates on a single sample of real data. | Channel equalization, servo control, linear predictive coding.
IIR | Infinite impulse response filter that operates on a single sample of real data. | Audio processing, general filtering.
Vector Dot Product | Sum of the pointwise multiplication of two vectors. | Convolution, correlation, matrix multiplication, multi-dimensional signal processing.
Vector Add | Pointwise addition of two vectors, producing a third vector. | Graphics, combining audio signals or images.
Vector Maximum | Find the value and location of the maximum value in a vector. | Error control coding, algorithms using block floating-point.
Viterbi Decoder | Decode a block of bits that has been convolutionally encoded. | Error control coding.
Control | A sequence of control operations (test, branch, push, pop, and bit manipulation). | Virtually all DSP applications include some control code.
256-Point In-Place FFT | Fast Fourier Transform converts a time-domain signal to the frequency domain. | Radar, sonar, MPEG audio compression, spectral analysis.
Bit Unpack | Unpacks variable-length data from a bit stream. | Audio decompression, protocol handling.
Notes: Why BDTI

## Slide 4: Benchmarking methodology
Comparison target: Texas Instruments TMS320C55x
Both implementations assume all data is in on-chip dual-access RAM
Performance is evaluated with cycle counts
HARSP don’t implement bit manipulation => only “Viterbi decoder” metric update part is estimated.
Notes: Why TI: Publicly available documentation, Market Leader, Full coverage of BDTI Kernel Benchmarks with cycle count performance evaluation.
HARSP has no bit manipulation instructions, thus we could not implement this part of the benchmark suite

## Slide 5: Real block FIR
Algorithm
x – input samples block
h – filter coefficients block
nh – number of filter coefficients
nx – number of samples
Features: Single MAC-block is used
TI C55x benchmark
Core: nx * (2 + nh)
Overhead: 25
HARSP benchmark
Core: nx * (1 + nh)
Overhead: 12

## Slide 6: Real block FIR
Algorithm
x – input samples block
h – filter coefficients block
nh – number of filter coefficients
nx – number of samples
Features: Dual MAC-block is used
TI C55x benchmark
Core: nx/2 * (6 + nh)
Overhead: 25
HARSP benchmark
Core: nx/2 * (1 + nh)
Overhead: 12

## Slide 7: Real Single-Sample FIR
Algorithm
x – input sample and filter memory
h – filter coefficients block
nh – number of filter coefficients
nx – number of samples = 1 (real-time filtering)
Features: Single MAC-block is used
TI C55x benchmark
Core: (1 + nh)
Overhead: 44
HARSP benchmark
Core: (1 + nh)
Overhead: 15

## Slide 8: Real Single-Sample FIR
Algorithm
x – input sample and filter memory
h – filter coefficients block
nh – number of filter coefficients
nx – number of samples = 1 (real-time filtering)
Features: Dual MAC-block is used
TI C55x benchmark
Core: (1 + nh/2)
Overhead: 44
HARSP benchmark
Real-time
Core: (3 + nh/2)
Overhead: 15
Quasi Real-time
Core: (1 + nh/2)
Overhead: 24
Notes: Quasi-Realtime: 2 input samples result in 2 outputs every 2 steps

## Slide 9: Complex block FIR
Algorithm
x – input samples block
h – filter coefficients block
nh – number of filter coefficients
nx – number of samples
Features: Dual MAC-block is used
TI C55x benchmark
Core: nx * [8 + 2*(nh-2)]
Overhead: 51
HARSP benchmark
Core: nx * (1 + 2*nh)
Overhead: 14

## Slide 10: LMS Adaptive FIR
Algorithm
x – input samples block
h – filter coefficients block
des – destination vector
e – current step error
µ - correction coefficient
nh – number of filter coefficients
nx – number of samples
Features: Dual MAC-block is used
TI C55x benchmark
Core: nx * (5 + 2*nh)
Overhead: 26
HARSP benchmark
Core: nx * (4 + 3*nh)
Overhead: 12

## Slide 11: Double Precision IIR in Form II
Algorithm
x – input samples memory
nx – number of samples
This form of filter’s one section is called biquad
a1, a2, b0, b1, b2 – biquad coefficients
nbiq – number of filter sections (biquads)
Features: Dual MAC-block is used, 5 coefficients
TI C55x benchmark
Core: nx * (7 + 31*nbiq)
Overhead: 77
HARSP benchmark
Core: nx * (4 + 21 * nbiq)
Overhead: 12

## Slide 12: Single Precision IIR in Form II
Algorithm
x – input samples memory
nx – number of samples
This form of filter’s one section is called biquad
a1, a2, b0=1, b1, b2 – biquad coefficients
nbiq – number of filter sections (biquads)
Features: Dual MAC-block is used, 4 coefficients
TI C55x benchmark
Core: nx * (2 + 3*nbiq)
Overhead: 44
HARSP benchmark
Core: nx * (2 + 5*nbiq)
Overhead: 12

## Slide 13: Single Precision IIR in Form II
Algorithm
x – input samples memory
nx – number of samples
This form of filter’s one section is called biquad
a1, a2, b0, b1, b2 – biquad coefficients
nbiq – number of filter sections (biquads)
Features: Dual MAC-block is used, 5 coefficients
TI C55x benchmark
Core: nx * (5 + 5*nbiq)
Overhead: 60
HARSP benchmark
Core: nx * (2 + 6*nbiq)
Overhead: 12

## Slide 14: Single Precision IIR in Form I
Algorithm
x – input samples memory
nx – number of samples
a1, a2, b0, b1, b2 – biquad coefficients
nbiq – number of filter sections (biquads)
Features: Dual MAC-block is used, 5 coefficients
TI C55x benchmark
Core: nx * (5 + 8*nbiq)
Overhead: 68
HARSP benchmark
Core: nx * (1 + 7*nbiq)
Overhead: 12

## Slide 15: Vector Maximum
Algorithm
Find maximum value and its index at input vector x
x – input vector
nx – number of elements in vector
Features: Dual MAC-block is used
TI C55x benchmark
Core: nx * 3
Overhead: 8
HARSP benchmark
Core: nx * 5
Overhead: 12

## Slide 16: Viterbi Decoder
Algorithm:
GSM Half Rate Convolutional Encoder (R=1/2, K=5, Frame=189)
Metrics Update part is estimated
SD – soft-decision inputs
G – expected inputs for each path state
j – indicator of the path
C – inverse of coding rate
Features: Dual MAC-block is used
TI C55x benchmark
Core: Frame*34
Overhead: 121
HARSP benchmark
Core: Frame*109
Overhead: N/A
Notes: Very rough estimate

## Slide 17: 256-Point-In-Place FFT
Algorithm: Radix-2 decimation-in-time FFT
N – number of samples
Features: No hardware acceleration at TI C55x is used
TI C55x benchmark
Core: 5*N/2*log2N
Overhead: N/A
HARSP benchmark
Core: 4*N/2*log2N
Overhead: N/A

## Slide 18: Benchmarking results
Function | Cycles benchmark | 
 | C55x | HARSP
Block FIR 1 MAC | C: nx * (2 + nh) O: 25 | C: nx * (1 + nh) O: 12
Block FIR 2 MAC | C: nx/2 * (6 + nh) O: 25 | C: nx/2 * (1 + nh) O: 12
Single Sample FIR 1 MAC | C: (1 + nh) O: 44 | C: (1 + nh) O:15
Single Sample FIR 2 MAC | C: (1 + nh/2) O: 24 | C: (3 + nh/2) O: 15
Quasi-realtime Single Sample FIR 2 MAC | - | C: (1 + nh/2) O: 24
Complex Block FIR | C: nx * [8 + 2*(nh-2)] O: 51 | C: nx * (1 + 2*nh) O: 14
LMS Adaptive FIR | C: nx * (5 + 2*nh) O: 26 | C: nx * (4 + 3*nh) O: 12
IIR Double Precision Form II | C: nx * (7 + 31*nbiq) O: 77 | C: nx * (4 + 21*nbiq) O: 12

## Slide 19: Benchmarking results
Function | Cycles benchmark | 
 | C55x | HARSP
IIR 4 Coefficient Form II | C: nx * (2 + 3*nbiq) O: 44 | C: nx * (2 + 5*nbiq) O: 12
IIR 5 Coefficient Form II | C: nx * (5 + 5*nbiq) O: 60 | C: nx * (2 + 6*nbiq) O: 12
IIR 5 Coefficient Form I | C: nx * (5 + 8*nbiq) O: 68 | C: nx * (1 + 7*nbiq) O: 12
Vector Dot Product | C: nx + 1 O: 44 | C: nx + 1 O: 15
Vector Add | C: nx * 3 O: 23 | C: nx * 2 O: 14
Vector Maximum | C: nx * 3 O: 8 | C: nx * 5 O: 12
Viterbi Decoderd | C: Frame * 34 O: 121 | C: Frame * 109 O: n/a
256-Point In-Place FFT | C: 5 * N/2 * log2N | C: 4 * N/2 * log2N

## Slide 20: Conclusions
The results of HARSP benchmarking suggest that the architecture is viable and has good performance potential in the DSP domain
The benchmarking revealed a number of architectural problems
We have developed a set of suggestions for HARSP development, which will allow us to achieve the desired performance level
We see further development of HARSP in developing our own highly optimized DSP library based on kernel benchmarks

## Slide 21: Contacts
  Director: Academician Igor Sokolov
  Address: Institute of Informatics Problems, Federal Research Center “Computer Science and Control" of the Russian Academy of Sciences,
  44 b.2 Vavilova str., Moscow, 119333
Phone: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: isokolov@ipiran.ru
Speaker: Shikunov Yury yishikunov@gmail.com