## Slide 1
Self-Timed Fused Multiply-Add Unit Performance Improvement
Institute of Informatics Problems, Federal Research Center
"Computer Science and Control" of the Russian Academy of Sciences
I. Sokolov, Y. Stepchenkov, Y. Rogdestvenski, Y. Diachenko, A. Rogdestvenskene, D. Diachenko

## Slide 2: Content
What are the Self-timed circuits?
Fused multiply-add (FMA) unit structure
How can we accelerate self-timed FMA?
Practical techniques improving self-timed FMA’s performance
Conclusions
ElConRus2022 2 of 22

## Slide 3: Self-Timed Circuits
ElConRus2022 3 of 22
They are free of global synchronization and operate based on a request-acknowledge interaction between circuit parts.
Major principles:
two-phase work discipline,
mandatory detection and acknowledging completion of all switches initiated during the transition to the current phase of work

## Slide 4: Self-Timed Circuit’s Advantages
ElConRus2022 4 of 22
Absence of a global clock tree accounting for up to 30% of total power consumption
Absence of "races" between internal signals
Correct operation under any operating conditions (supply voltage and ambient temperature)
Their performance is determined by the actual logic cells' delays in the current operating conditions, not the worst case

## Slide 5: Self-Timed Circuit’s Drawbacks
ElConRus2022 5 of 22
Increased hardware complexity because of redundant data coding and indication subcircuit
Two-phase operation mode decelerates self-timed circuit’s total performance
Indication subcircuit causes an additional delay increasing in multi-bit units
Direct conversion of synchronous circuits to self-timed ones can lead to ineffective solutions in performance or an excessive hardware costs

## Slide 6: Fused multiply-add (FMA) unit
ElConRus2022 6 of 22
C[63:0]
A[63:0]
B[63:0]
Align
A  B
3:2 CSA
Adder
LZA
Round & Post-Normalizer
Normalizer
Result

## Slide 7: Cases simplifying calculations
ElConRus2022 7 of 22
exp(C)  exp(A  B ) | Result | Normalization order | Round
[57, ) | C |  | 
[2, 56] | A  B  aligned_C | n | +
[1, 1] | A  B  aligned_C | n | +
[55, 2] | A  B  C | 1 | +
(, 56] | A  B | 1 | +

## Slide 8: Self-Timed Fused Multiply-Add-Subtract (FMAS) Unit
ElConRus2022 8 of 22
A, B, C – input operands
R – operation options
Wr – force write input
Rst – asynchronous reset
WrEn – write enable output
RqO – result ready output
FMA – multiply-add result
FMS – multiply-subtract result
RFA – flags of FMA operation
RFS – flags of FMS operation
AckO – read result acknowledging
  IEEE 754 Standard Compliant
  Ternary multiplier and adder-subtractor

## Slide 9: Increasing FMAS Performance (1)
ElConRus2022 9 of 22
  Ternary coding simplifies and accelerates adding-subtracting multi-bit operands

## Slide 10: Increasing FMAS Performance (2)
ElConRus2022 10 of 22
  Rule 1: Do not tie the estimated operating time of individual units and pipeline stages to the maximum time for the worst operating conditions, but use the statistically average operating time.
  Rule 2: Use new algorithmic solutions that may be ineffective in synchronous circuitry as they decrease the unit's performance in the worst case.
  An important feature of the self-timed circuits: their operation time depends on the processed data

## Slide 11: Increasing FMAS Performance (3)
ElConRus2022 11 of 22
  The ways to increase self-timed FMAS performance:
  • Using LZA pre-calculation with reduced bit-width
  • Reducing bit-width of output registers for sum and difference of the product and the third operand due to parallelization of data processing.
  • Speeding up normalization and post-normalization.

## Slide 12: Optimized Normalization (1)
ElConRus2022 12 of 22
  The main idea of the proposed improvement:
  Align the largest of the third operand or product in the most significant bits of the adder-subtractor,
  Shift the rest one by order corresponding to the difference of their exponents.

## Slide 13: Optimized Normalization (2)
ElConRus2022 13 of 22
  Typical algorithm for the case “exp(C) – exp(A  B)”  [2, 56]
  55
  107 0
  A  B
  107 55
  C
  160 52 0
  55 0
  Normalization
  52 0
  Rounding
  
  Normalization order  107
  Shift by order [2, 56]

## Slide 14: Optimized Normalization (3)
ElConRus2022 14 of 22
  Proposed algorithm for the case “exp(C) – exp(A  B)”  [2, 56]
  107 55
  A  B
  160 108
  C
  160 55
  55 0
  Normalization
  52 0
  Rounding
  
  Normalization order  57 !
  Shift by order [2, 56]

## Slide 15: Optimized Normalization (4)
ElConRus2022 15 of 22
  Typical algorithm for the case “exp(C) – exp(A  B)”  [–56, –2]
  107 0
  A  B
  107 55
  C
  160 0
  55 0
  Normalization
  52 0
  Rounding
  
  Normalization order  107
  Shift by order [2, 56]

## Slide 16: Optimized Normalization (5)
ElConRus2022 16 of 22
  Proposed algorithm for the case “exp(C) – exp(A  B)”  [–56, –2]
  160 52
  A  B
  160 108
  C
  Shift by order [2, 56]
  160 52
  55 0
  Normalization
  52 0
  Rounding
  
  Normalization order  57 !

## Slide 17
ElConRus2022 17 of 22
  Optimization results:
  1. The bit-width of the operand to be normalized is reduced from 161 to 106
  2. The duration of all basic operations of the critical cycle is decreased by 15 – 20 %
  3. Hardware complexity of the self-timed fused multiply-add-subtract unit is efficiently reduced
Optimized Normalization (6)

## Slide 18
ElConRus2022 18 of 22
Ternary Wallace Tree
  1-st stage
  2-nd stage
  80 S16,27 0
  80 S0,15 0
  26 bits

## Slide 19: Carry Propagation Paths in the Ternary Adder
ElConRus2022 19 of 22
Hi Bi
A D
B Ind
Ho Bo
Hi Bi
A D
B Ind
Ho Bo
Hi Bi
A D
B Ind
Ho Bo

## Slide 20: LZA Unit
ElConRus2022 20 of 22
24-bit Subtraction
Leading zeros counting (NLZ)
  23 0
  A  B
  C
  23 0
  
  “000010110…”
  NLZ < 24 ?
  No
  Yes
Normalization order = NLZ
Normalization order must be calculated
  Part 1
  Part 2

## Slide 21: Conclusions
Self-timed circuit operation discipline allows for wider using speculative result calculation techniques on a base of detailed specifying the possible cases of the input operands ratio
The proposed normalization technique reduces a bit-width of processed data (by 1.5 times), duration of all primary operations of the critical cycle (in 15-20%), and hardware complexity (in 20-25%)
Preliminary estimation of the leading zero number of the most significant bits of product and third operand (24 for double precision or 12 for single precision) decreases by 32% an average delay, added by normalization pipeline stage to total Fused Multiply-Add-Subtract unit’s delay
ElConRus2022 21 of 22

## Slide 22: Contacts
  Director: Academician Igor Sokolov
  Address: Institute of Informatics Problems, Federal Research Center “Computer Science and Control" of the Russian Academy of Sciences,
  44 b.2 Vavilova str., Moscow, 119333
Phone: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: isokolov@ipiran.ru
Speaker: Diachenko Yury diaura@mail.ru
ElConRus2022 22 of 22