## Slide 1
Self-Timed Storage Register Cases
Institute of Informatics Problems, Federal Research Center
"Computer Science and Control" of the Russian Academy of Sciences
Yuri G. Diachenko, Yuri I. Shikunov, Nikolai V. Morozov Denis Y. Diachenko, Dmitri Y. Stepchenkov

## Slide 2: Content
What are the Self-Timed circuits?
Self-timed pipeline
Self-timed storage register basis
Self-timed storage register implementation cases
Conclusions
EDM2022 2 of 23

## Slide 3: Self-Timed Circuits
EDM2022 3 of 23
They are free of global clock and operate based on a request-acknowledge interaction between circuit parts.
Major principles:
two-phase operation discipline,
mandatory detection and acknowledging completion of all switches initiated during the transition to the current phase of work
Self-timed circuits are the hopeful alternate of synchronous circuits in designing reliable digital systems

## Slide 4: Self-Timed Circuit’s Advantages
EDM2022 4 of 23
Absence of a global clock tree accounting for up to 30% of total power consumption
Absence of hazards and "races" between signals
Correct operation under any operating conditions (supply voltage and ambient temperature)
Their performance is determined by the actual logic cells' delays in the current operating conditions, not the worst case
Better soft error tolerance

## Slide 5: Self-Timed Circuit’s Drawbacks
EDM2022 5 of 23
Increased hardware complexity because of redundant data coding and indication subcircuit
Two-phase operation mode decelerates self-timed circuit’s total performance
Indication subcircuit causes an additional delay increasing in multi-bit units
Only careful design, including appropriate algorithms and circuitry, can ensure the effective self-timed implementations

## Slide 6: Self-Timed Pipeline
EDM2022 6 of 23
CPi – i-th pipeline stage’s combinational part
ORi – i-th pipeline stage’s output register
CPIi – the Cpi’s indication subcircuit
ORIi – the ORi’s indication subcircuit
C – Muller’s C-element
Indication subcircuits and C-elements ensure request-acknowledge interaction between self-timed circuits

## Slide 7: ST Storage Register Features
EDM2022 7 of 23
Keeping the working and spacer state until the subsequent ST circuit’s acknowledgment
Dual-rail output code generation if the subsequent circuit is a combinational one, otherwise, the output can be of any self-timed type
Forcing all register bits into the spacer (optional)
Presetting or resetting register bits in common or individual mode (optional)

## Slide 8: Static two-input C-element
EDM2022 8 of 23
Q+ = I0I1 + Q(I0 + I1)
12 CMOS transistors

## Slide 9: Static C-element with Reset
EDM2022 9 of 23
Q+ = R(I0I1 + Q(I0 + I1))
14 CMOS transistors

## Slide 10: Static C-element with Preset
EDM2022 10 of 23
Q+ = I0I1 + Q(I0 + I1) + S
14 CMOS transistors

## Slide 11: Static C-element with both Reset and Preset
EDM2022 11 of 23
Q+ = R(I0I1 + Q(I0 + I1) + S)
16 CMOS transistors

## Slide 12: ST Register Bit on RS-latch (1)
EDM2022 12 of 23
(R, S) and (Q, QB) – the bi-stable information signals,
E – an acknowledgement signal from a subsequent circuit,
RT – an asynchronous reset,
I – an indication output
26 CMOS transistors

## Slide 13: ST Register Bit on RS-latch (2)
EDM2022 13 of 23
(R, S) and (Q, QB) – the dual-rail information signals with null spacer,
E – an acknowledgement signal from a subsequent circuit,
RT – an asynchronous reset,
I – an indication output
42 CMOS transistors

## Slide 14: Dual-Rail Coding
EDM2022 14 of 23
X | XB | State
0 | 0 | Null spacer
0 | 1 | Bit 0
1 | 0 | Bit 1
1 | 1 | Unit spacer
Any dual-rail information signal has only one spacer, either null or unit!
X
XB
X
XB
Indication
I
I

## Slide 15: ST Register Bit on RS-flip-flop
EDM2022 15 of 23
(R, S) and (Q, QB) – the dual-rail information signals with null spacer, E – an acknowledgement signal from a subsequent circuit,
RT – an asynchronous reset,
I – an indication output
60 CMOS transistors

## Slide 16: ST Register Bit on C-elements (1)
EDM2022 16 of 23
(X, XB) and (Q, QB) – the dual-rail information signals with null spacer, E – an acknowledgement signal from a subsequent circuit,
I – an indication output
28 CMOS transistors
1.5 – 2.1 times simpler than other cases !!

## Slide 17: ST Register Bit on C-elements (2)
EDM2022 17 of 23
Request-Acknowledge interaction
Data
Spacer
Data
Spacer
Data
Spacer
Data
Spacer
Data
Spacer
Data
Spa
cer
X, XB
E (Ack)
Q, QB
I (Req)

## Slide 18: ST Register with no preset
EDM2022 18 of 23
Null spacer
Unit spacer

## Slide 19: Multi-input Indication subcircuit
EDM2022 19 of 23

## Slide 20: ST Register with Reset to Spacer
EDM2022 20 of 23
Null spacer
Unit spacer

## Slide 21: ST Register with Bit-Wise Preset
EDM2022 21 of 23
Null spacer
Unit spacer

## Slide 22: Conclusions
Muller’s C-element is the best basis for the self-timed storage register implementation as it decreases register’s complexity in 1.5 through 2.1 times compared to RS-latch and RS-flip-flop counterparts.
The proposed C-element cases on CMOS transistors provide typical self-timed storage register implementations with different options
The self-timed storage register on C-elements provides minimal hardware redundancy at a factor of 1.4 compared to synchronous counterparts while combinational self-timed circuits have the hardware redundancy at a factor of 2.5 through 3
EDM2022 22 of 23

## Slide 23: Contacts
  Director: Academician Igor Sokolov
  Address: Institute of Informatics Problems, Federal Research Center “Computer Science and Control" of the Russian Academy of Sciences,
  44 b.2 Vavilova str., Moscow, 119333
Phone: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: isokolov@ipiran.ru
Speaker: Diachenko Yuri, diaura@mail.ru
EDM2022 23 of 23