## Slide 1
Self-Timed Pipeline with Variable Stage Number
Institute of Informatics Problems, Federal Research Center
"Computer Science and Control" of the Russian Academy of Sciences
I. Sokolov, Y. Stepchenkov, Y. Diachenko, Y. Rogdestvenski, D. Diachenko, L. Plekhanov

## Slide 2: Outline
Self-timed circuits vs Synchronous ones
Synchronous and self-timed pipelines
Bypassing pipeline stages
Self-timed pipeline bypass technique
Conclusions
EIConRus2023 2 of 20

## Slide 3: Self-Timed Circuits
EIConRus2023 3 of 20
They are free of global synchronization and operate based on a request-acknowledge interaction between circuit parts.
Major principles:
two-phase work discipline,
Mandatory acknowledging completion of all switches initiated during the transition to the current phase of work

## Slide 4: Self-Timed Circuit’s Advantages
EIConRus2023 4 of 20
Absence of a global clock tree accounting for up to 30% of total power consumption
Absence of glitches and hazards
Correct operation under any operating conditions
High performance determined by the actual cells' delays in the current operating conditions, not the worst case

## Slide 5: Simple Synchronous Pipeline
EIConRus2023 5 of 20
S1
S3
SN−1
SN
…
DataIn
DataOut
Clock
S2
Stages S2 and S3 are the slowest
Pipeline’s delay (latency) = N∙Tclock
Output result’s periodicity = Tclock
Tclock – Global clock period for worst conditions

## Slide 6: Synchronous Pipeline with Bypass
EIConRus2023 6 of 20
Pipeline’s average delay = (PBP∙2+PFull∙N)∙Tclock , where PBP and PFull are path probabilities (PBP + PFull = 1)
Output result’s periodicity = Tclock
S1
S2
SN−1
…
DataIn
DataOut
Clock
MX
SN
Control

## Slide 7: Simple Self-Timed (ST) Pipeline
EIConRus2023 7 of 20
Stages S2 and S3 are the slowest
Pipeline’s delay = N∙Tphase2
Output result’s periodicity = 4∙Tphase2
Tphase2 – actual S2 stage’s switch-to-phase duration
S1
R A
S3
R A
SN−1
R A
SN
R A
…
DataIn
DataOut
Ack
S2
R A
Req
…

## Slide 8: ST Pipeline’s Phase Diagram
1 | S | W |  | S |  | W |  | S |  | W |  | S |  | W |  | S |  |  | 
2 | S |  | W |  | S |  | W |  | S |  | W |  | S |  | W |  | S |  | 
3 | S |  |  | W |  | S |  | W |  | S |  | W |  | S |  | W |  | S | 
4 | S |  |  |  | W |  | S |  | W |  | S |  | W |  | S |  | W |  | S
5 | S |  |  |  |  | W |  | S |  | W |  | S |  | W |  | S |  | W | 
6 | S |  |  |  |  |  | W |  | S |  | W |  | S |  | W |  | S |  | W
EIConRus2023 8 of 20
“S” – spacer phase;
“W” – working phase;
others – waiting
Output period = 4Tphase2
Latency = 6Tphase2
Previous and subsequent stages affect the current stage’s phase switching

## Slide 9: ST Pipeline Stage
EIConRus2023 9 of 20
CP– combinational part;
Rg – output register;
C – Muller’s C-element
A – acknowledge output;
E – register’s control signal;
R – request input
CP
Ind
DataIn
Rg
E Ind
C
C
A
R
DataOut
Register indicates all CP’s information outputs
E

## Slide 10: ST Pipeline Stage’s Register Bit
EIConRus2023 10 of 20
(X, XB) – dual-rail information input,
(Y, YB) – dual-rail information output,
E – phase-enable signal,
Ind – indication output
Ind
Null spacer
C
X
C
1
E
XB
Y
YB
Unit spacer
C
X
C
&
E
XB
Y
Ind
YB

## Slide 11: One ST Pipeline Stage Bypass
EIConRus2023 11 of 20
And – multi-bit logical “AND” function;
MX – multi-bit multiplexer;
BPC – bypass control unit
S1
R A
S2
R A
E
S3
R A
DataIn
DataOut
Ack
And
Req
MX
BPC
L A3
E2
A1 U
R1 A2

## Slide 12: Bypass Control Unit
EIConRus2023 12 of 20
L – dual-rail pipeline bypass mode signal;
A1, A2, A3 – acknowledge outputs of the stages;
E2 – stage S2 register’s control signal;
R1 – S1 stage’s request input;
U, UB – dual-rail bypass marker
U
R1
L
A2
A3
C
C
& 1
& 1
& 1
1 &
&
Self-timed RS-latch
A1
E2
UB

## Slide 13: ST Pipeline’s Phase Diagram
1 | S | W |  | S |  | W |  |  | S |  | W |  | S |  | W |  | S |  |  | 
2 | S |  | W |  | S |  |  |  |  |  |  | W |  | S |  |  |  |  |  | 
3 | S |  |  | W |  | S |  | W |  | S |  |  | W |  | S |  | W |  | S | 
4 | S |  |  |  | W |  | S |  | W |  | S |  |  | W |  | S |  | W |  | S
5 | S |  |  |  |  | W |  | S |  | W |  | S |  |  | W |  | S |  | W | 
6 | S |  |  |  |  |  | W |  | S |  | W |  | S |  |  | W |  | S |  | W
EIConRus2023 13 of 20
Every second input data bypasses the slowest stage S2
Average output period = 3Tphase,S2+1.5Tphase,S1
Average latency = 3.5Tphase,S2+2.5Tphase,S1
Output periodicity and Latency become less!

## Slide 14: Two ST Pipeline Stages Bypass
EIConRus2023 14 of 20
And – multi-bit logical “AND” function;
MX – multi-bit multiplexer;
BPC – bypass control unit
DataIn
S1
R A
S2
R A
E
S4
R A
DataOut
Ack
And
Req
MX
S3
R A
E
BPC
L A4
A2
A1 E2
E3
R1 U

## Slide 15: Two-Stage Bypass Control Unit
EIConRus2023 15 of 20
L – dual-rail pipeline bypass mode signal;
A1, A2, A4 – acknowledge outputs of the stages;
E2, E3 – stage register’s control signals;
R1 – S1 stage’s request input;
U, UB – dual-rail bypass marker
U
R1
L
A1
E2
C
C
& 1
& 1
& 1
1 &
&
Self-timed RS-latch
A4
A2
R
C
E3
UB

## Slide 16: ST Pipeline’s Phase Diagram
1 | S | W |  | S |  | W |  |  |  | S |  | W |  | S |  | W |  |  |  | S |  | W
2 | S |  | W |  | S |  |  |  |  |  |  |  | W |  | S |  |  |  |  |  |  | 
3 | S |  |  | W |  | S |  |  |  |  |  |  |  | W |  | S |  |  |  |  |  | 
4 | S |  |  |  | W |  | S |  | W |  | S |  |  |  | W |  | S |  | W |  | S | 
5 | S |  |  |  |  | W |  | S |  | W |  | S |  |  |  | W |  | S |  | W |  | S
6 | S |  |  |  |  |  | W |  | S |  | W |  | S |  |  |  | W |  | S |  | W | 
EIConRus2023 16 of 20
Every second input data bypasses the slowest stages S2 and S3
Average output period = 2Tphase,S2+3Tphase,S1
Average latency = 2.5Tphase,S2+3.5Tphase,S1
Output periodicity and Latency become less!

## Slide 17: ST Pipeline’s Performance
EIConRus2023 17 of 20
Case | A | B | C
Average output periodicity | 4T0 | (3 + 1.5k)T0 | (2 + 3k)T0
Average latency | 6T0 | (3.5 + 2.5k)T0 | (2.5 + 3.5k)T0
Pipeline performance comparison for the cases:
A - typical 6-stage pipeline with the slowest stages S2 and S3;
B - the same pipeline with regular bypassing stage S2;
C - the same pipeline with regular bypassing stages S2 and S3,
in the following assumptions:
Tphase,S1 = Tphase,S4 = Tphase,S5 = Tphase,S6 = kT0, k < 1,
Tphase,S2 = Tphase,S3 = T0,
Bypass occurs every second input data portion.

## Slide 18: ST Pipeline’s Performance
EIConRus2023 18 of 20
Average output periodicity, T0
k
k
Average latency, T0
Chart: 
| 0.1 | 0.2 | 0.3000000000000001 | 0.4 | 0.5 | 0.6000000000000002 | 0.70000000000000018 | 0.8 | 0.9 | 1
A | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
B | 3.15 | 3.3 | 3.45 | 3.6 | 3.75 | 3.9 | 4.05 | 4.2 | 4.35 | 4.5
C | 2.3 | 2.6 | 2.9 | 3.2 | 3.5 | 3.8 | 4.1 | 4.4 | 4.7 | 5
Chart: 
| 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.60000000000000009 | 0.70000000000000007 | 0.8 | 0.9 | 1
A | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6
B | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5 | 5.25 | 5.5 | 5.75 | 6
C | 2.85 | 3.2 | 3.55 | 3.9 | 4.25 | 4.6 | 4.95 | 5.3 | 5.65 | 6
A - typical 6-stage pipeline with the slowest stages S2 and S3;
B - the same pipeline with regular (each second sample) bypassing stage S2;
C - the same pipeline with regular bypassing stages S2 and S3,

## Slide 19: Conclusions
ST circuit pipeline organization increases its performance, similarly to synchronous circuits.
The optional bypass of one or more stages under some conditions ensures the average pipeline’s performance increase if the bypassed stages are sufficiently slowest among all pipeline stages.
The slower the stages being bypassed compared to the other stages, the lower the average output periodicity and latency of the self-timed pipeline.
ElConRus2023 19 of 20

## Slide 20: Contacts
  Director: Academician Igor Sokolov
  Address: Institute of Informatics Problems, Federal Research Center “Computer Science and Control" of the Russian Academy of Sciences,
  44 b.2 Vavilova str., Moscow, 119333
Phone: +7 (495) 137 34 94
Fax: +7 (495) 930 45 05
E-mail: isokolov@ipiran.ru
Speaker: Diachenko Yury diaura@mail.ru
ElConRus2023 20 of 20