## Slide 1
Self-Timed pipeline protection against critical fault
Institute of Informatics Problems, Federal Research Center
"Computer Science and Control" of the Russian Academy of Sciences
Y. Stepchenkov, Y. Diachenko, G. Appolonov, N. Morozov, D. Stepchenkov, D. Diachenko

## Slide 2: Fault Types
ElConRus2025 2 of 18
Faults
Soft errors
Self-disappeared
Critical
Failures
VDD
VSS
A
B
Ionization current:
Cosmic rays
Nuclear particles
Radiation
Noises:
Cross-talk
Power bus noise
Substrate noise

## Slide 3: Self-Timed Circuit Redundancy
EIConRus2025 3 of 18
Synchronous circuit
N Unary Inputs
Self-timed circuit
F
Output
2N Dual-rail Inputs
F
Ind
Indicator
F
Output
Inversed Output
Combinational self-timed circuits utilize the dual-rail data coding

## Slide 4: Self-Timed Pipeline
EIConRus2025 4 of 18
The ST pipeline interaction principle:
any pipeline stage can switch to the working (spacer) phase only after the subsequent stage has completed switching to the spacer (working) phase, and the information outputs of the preceding stage have switched to the working (spacer) phase
Ack – Acknowledgement output;
Req – Request input

## Slide 5: Self-Timed Pipeline Stage
EIConRus2025 5 of 18
NN | X | XB | State | 
 |  |  | Null Spacer | Unit Spacer
1. | 0 | 0 | Spacer | Antispacer
2. | 0 | 1 | Bit 0 | Bit 0
3. | 1 | 0 | Bit 1 | Bit 1
4. | 1 | 1 | Antispacer | Spacer
Dual-Rail Coding with Null and Unit Spacer
Req –Request input
Ack –Acknowledge output

## Slide 6: Muller’s C-element
EIConRus2025 6 of 18
C-element
Q+ = AB + Q(A + B)
(X, XB) and (Y, YB) – dual-rail signals with the same spacer;
E – phase input;
I – indication output
Register bit

## Slide 7: Self-Timed Pipeline Operation Diagram without Soft Errors
EIConRus2025 7 of 18
E – soft error signal;
(Din,DBin) – dual-rail input;
(Dout,DBout) – dual-rail output;

## Slide 8: ST Pipeline Operation Diagram with Antispacer
EIConRus2025 8 of 18
Soft error at T3 leads to an antispacer state when a working phase starts (at T4). Then antispacer gets a register bit, propagates to the pipeline output (Dout,DBout) and stops the pipeline operation

## Slide 9: Modified Muller’s C-element
EIConRus2025 9 of 18
Modified C-element circuit
Symbol view
Register bit

## Slide 10: ST Pipeline Diagram with Modified C-element and SE at Spacer Phase
EIConRus2025 10 of 18
Soft error at T3 leads to an antispacer state when a working phase starts (at T4). However, the pipeline continue to operate when soft error ends.

## Slide 11: ST Pipeline Diagram with Modified C-element and SE at Working Phase
EIConRus2025 11 of 18
Soft error at the working phase (at T1) leads to an incorrect working state starts (at T3). Modified C-element does not repair it after soft error ends.

## Slide 12: Improved Muller’s C-element
EIConRus2025 12 of 18
Additional transistor prevents the anti-spacer writing into register bit.

## Slide 13: ST Pipeline Diagram with Improved C-element and SE at Working Phase
EIConRus2025 13 of 18
Register bit affected by the soft error does not switch to the anti-spacer and remains in the correct working state that prevents output data corruption.

## Slide 14: ST Pipeline Diagram with Improved C-element and SE at Spacer Phase
EIConRus2025 14 of 18
Soft error at the spacer phase corrupts the pipeline’s output data.

## Slide 15: ST Pipeline with Improved Protection against Soft Errors
EIConRus2025 15 of 18
Indication output of each pipeline stage delays the subsequent stage's request input switch, thus increasing soft error masking propability.

## Slide 16: Improved ST Pipeline Diagram with Soft Error at Spacer Phase
EIConRus2025 16 of 18
Soft error appeared at the spacer phase does not corrupt output data, and only increases working phase’s duration.

## Slide 17: Conclusions
Due to the two-phase discipline and redundant coding of information signals, the self-timed pipeline successfully masks a significant part of the soft errors.
Using the advanced Muller's C-element as a storage cell in the self-timed pipeline stage register bit increases pipeline’s fault tolerance level and prevents the pipeline's stall.
The forced delay of the stage register's write enable signal using the preceding stage's indication output masks the soft error at the spacer phase. The penalty for obtained fault tolerance increase is 19% decrease in the pipeline's performance.
ElConRus2025 17 of 18

## Slide 18: Thanks for Your Attention !
ElConRus2025 18 of 18